## Slide 1
PLATFORM ARCHITECTURE & STANDARDIZED WORKFLOWS
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
01 / 20
SwiftFlow + HawkeyePlus
Standardized Inspection & Measurement
Architecture, Workflows & Integrated Delivery
SwiftFlow
Equipment, processes and execution
HawkeyePlus
Data, models and validation
+
From hardware design to algorithms and production workflows
2026.10
Notes: Introduce the complete title: SwiftFlow + HawkeyePlus — Standardized Inspection & Measurement: Architecture, Workflows & Integrated Delivery. Explain the shared concept and rationale, then the execution platform and model-development platform, followed by joint acceptance and a delivery baseline.

## Slide 2
ROADMAP / SWIFTFLOW + HAWKEYEPLUS
Presentation Roadmap
Start with a shared method, then explore the two platforms and their handoff
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
02 / 20
01
Vision & Rationale
Establish a shared engineering method
Platform roles
Why standardize
03–06
02
SwiftFlow
Equipment, workflows and algorithm execution
Equipment integration
Workflow design
07–10
03
HawkeyePlus
Industrial vision model development and validation
Model development
Model portfolio
11–16
04
Integrated Delivery
From development results to production readiness
Adaptation & acceptance
Shared delivery assets
17–18
Closing: Summary & Discussion
19–20
Notes: The presentation has four chapters: Vision & Rationale, SwiftFlow, HawkeyePlus, and Integrated Delivery, followed by a summary and discussion. Each agenda card links to its chapter divider in slideshow mode.

## Slide 3
CHAPTER 01 / OVERVIEW
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
03 / 20
01
Vision & Rationale
Establish a shared engineering method
How do hardware, workflows and algorithms work as one method?
01.1
Platform roles
01.2
Why standardize
01.3
Standard workflow
SwiftFlow + HawkeyePlus | One shared method, two complementary platforms
Notes: Chapter transition: Vision & Rationale. Focus: Establish a shared engineering method. Guiding question: How do hardware, workflows and algorithms work as one method?.

## Slide 4
CHAPTER 01 / VISION & RATIONALE
One Standard Workflow for Inspection & Measurement
Connect hardware design, inspection workflows and algorithm development through two complementary platforms
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
04 / 20
SwiftFlow
Equipment integration
Workflow orchestration
Inspection execution
Turn hardware, algorithms and process logic into executable workflows
HawkeyePlus
Data & annotations
Model training
Validation & release
Turn industrial images into validated, deliverable models
Samples
Models
Shared method: Define the goal → Design & build → Adapt & validate → Standardize delivery
Inspection
Defect location · Type · Decision
Measurement
Dimensions · Height · Geometry
Traceable delivery
Configuration · Version · Evidence
Notes: Two complementary platforms support one engineering method. SwiftFlow organizes equipment, workflows, classical vision, inference and results into execution. HawkeyePlus manages training data, model development, evaluation and versions. The arrows represent curated samples and validated model handoffs, not an already implemented automatic connector.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 5
CHAPTER 01 / VISION & RATIONALE
Why a Shared Engineering Method Matters
Make inputs, deliverables and acceptance criteria clear at every step
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
05 / 20
Align engineering inputs
Align hardware, imaging and algorithm needs
Common design inputs
Inspection / measurement goals
Image quality and calibration
Reuse proven work
Turn proven knowledge into reusable assets
Reusable deliverables
Device and workflow configuration
Models and algorithm parameters
Make acceptance explicit
Reproduce results on production equipment
Shared acceptance criteria
Independent samples and references
Quality, timing and traceable results
Standardization gives handoffs, reuse and maintenance a shared baseline
Define the method and delivery agreements; use both platforms to execute them
Notes: A shared method reduces repeated handoff work between hardware, process and algorithm engineering. These are design motivations, not measured claims about a team's productivity. Common inputs, reusable assets and joint acceptance make the required inputs, outputs and completion criteria clear.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 6
CHAPTER 01 / VISION & RATIONALE
From Engineering Goals to Standardized Delivery
Recommended workflow: clear inputs, engineering responsibilities and reviewable deliverables
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
06 / 20
01
Define goals
What to inspect or measure
Quality, timing and constraints
Requirements & acceptance
02
Design hardware
Camera, optics and lighting
Motion, sensing and calibration
Hardware design & samples
03
Design workflows
Positioning, capture and timing
Exceptions and result handling
Flow & device configuration
04
Develop algorithms
Classical vision / geometry
AI training and validation
Parameters / model package
05
Validate jointly
Site samples and references
Quality, metrology and timing
Acceptance evidence
06
Deliver a baseline
Configuration, models, versions
Traceable results and iteration
Reusable engineering assets
SwiftFlow
Equipment integration, commissioning, calibration, workflow execution and results
HawkeyePlus
Training data, model development, evaluation and model version management
Shared deliverables: hardware + workflow + algorithm baselines + acceptance evidence
Notes: This is a recommended engineering workflow, not a claim of an automated release system. Engineers design the hardware and imaging setup; SwiftFlow provides integration, commissioning, calibration and execution. Algorithms may be classical vision/numerical measurement or AI models developed in HawkeyePlus. Joint acceptance uses independent samples, detection errors and cycle-time checks, plus calibration, units and reference agreement for measurement.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 7
CHAPTER 02 / OVERVIEW
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
07 / 20
02
SwiftFlow
Equipment, workflows and algorithm execution
How can equipment and algorithms become an executable workflow?
02.1
Equipment integration
02.2
Workflow design
02.3
Inspection & measurement
SwiftFlow + HawkeyePlus | One shared method, two complementary platforms
Notes: Chapter transition: SwiftFlow. Focus: Equipment, workflows and algorithm execution. Guiding question: How can equipment and algorithms become an executable workflow?.

## Slide 8
CHAPTER 02 / SWIFTFLOW
SwiftFlow | Equipment & Process Execution
Use configurable workflows to connect equipment, classical vision, inference and results
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
08 / 20
Workflow design
Visual authoring
Reusable process flows
Shared execution engine
Sequential / parallel execution · Shared data
Run control · Failure handling
Algorithms & results
Classical vision + Model inference
Measurement + Result storage
Unified equipment integration
Standard interfaces · Multiple instances · Vendor adapters
Industrial cameras
Motion control
Controlled lighting
Height sensing
Optics / metrology
IO / Line communication
Cross-cutting support: logs & alarms · timing · traceability · storage · simulation
Notes: SwiftFlow is the workflow and execution foundation within HawkeyeUltra. Data-defined workflows combine equipment, vision, inference and result nodes, including subflows, parallel coordination and run control. Vendor-neutral interfaces and instance routing connect devices. Logs, timing, storage and results support execution.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 9
CHAPTER 02 / SWIFTFLOW
From Hardware Design to Executable Workflows
Translate hardware choices, commissioning and process knowledge into reusable configuration and workflows
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
09 / 20
Engineering design inputs
Camera / Optics / Lighting / Motion / Sensors
Define field of view, resolution, timing and calibration
Configuration & workflow implementation
Map device instances
Commission & calibrate
Reuse parameters & flows
Locate
Capture
Analyze
Decide & record
Deliver reusable engineering assets
Device mappings & configuration · Calibration · Workflows · Process parameters · Result definitions
Notes: Engineers start with camera, optics, lighting, motion and measurement-device design. Machine configuration maps physical devices to logical instances; commissioning and calibration establish input quality. Workflow nodes then organize positioning, acquisition, analysis and decisions. Deliverables include mappings, calibration and reusable process configuration. SwiftFlow is not a CAD or optical-design tool.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 10
CHAPTER 02 / SWIFTFLOW
One Workflow Foundation for Inspection & Measurement
Combine classical vision, AI and metrology as needed, sharing acquisition, orchestration and traceability
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
10 / 20
Inspection: locate defects and decide
Image → Classical vision / AI → Decision
Output: location, class and pass/fail
Measurement: produce defined metrics
Calibration → Capture / segmentation → Measurement
Output: dimensions, height and geometry
Shared foundation: acquire data → run algorithms → apply rules → retain results
Measurement requires calibration, units and reference validation; AI can assist localization or segmentation
Notes: Inspection and measurement share acquisition, orchestration and traceability, but produce different outputs. Inspection produces locations, classes and decisions; measurement produces defined dimensions, heights or geometric metrics. AI may assist localization or segmentation, but physical measurements still require calibration, units and measurement logic. Classical vision and laser/geometric measurement do not require AI training.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 11
CHAPTER 03 / OVERVIEW
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
11 / 20
03
HawkeyePlus
Industrial vision model development and validation
How do we turn data into validated, deliverable models?
03.1
Model development
03.2
Model portfolio
03.3
Validation & versions
SwiftFlow + HawkeyePlus | One shared method, two complementary platforms
Notes: Chapter transition: HawkeyePlus. Focus: Industrial vision model development and validation. Guiding question: How do we turn data into validated, deliverable models?.

## Slide 12
CHAPTER 03 / HAWKEYEPLUS
HawkeyePlus | Industrial Vision Model Development
Connect industrial images, model training, validation and release in one platform
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
12 / 20
01
Data & Annotations
Images + Labels / Masks
Import
Annotate
Preview
Visual Training Hub
Dataset
Model
Training
Job Setup
GPU Selection
Training Monitor
02
Validation & Delivery
Evaluate & Infer
Metrics · Prediction preview
Model Export
Convert · Package · Download
Model Registry
Product versions · Activation
Multi-framework Training
Compute & Asset Foundation
PaddlePaddle
Detect · Classify · Segment
PyTorch
Detect · Segment
anomalib
Anomaly Detection
Compute
GPU / Python
Data & Assets
Images · Weights · Logs
Management
Project ownership · User roles · Environment checks · GPU status · Storage quotas · Activity logs
Notes: HawkeyePlus combines dataset, model and training configurations, then starts the selected Python training backend. It manages jobs, monitoring, validation and model assets rather than implementing a new training algorithm. PaddlePaddle covers PaddleDetection/PaddleClas/PaddleSeg; PyTorch covers TorchDet/TorchSeg; anomalib is the PyTorch-based TorchAnomaly adapter. Compute selection does not imply distributed cluster scheduling.
These are training-platform capabilities. Integration into SwiftFlow requires runtime adaptation and acceptance.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 13
CHAPTER 03 / HAWKEYEPLUS
A Visual Lifecycle: From Data to Models
Bring preparation, training and validation into a shared model-development workflow
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
13 / 20
01
Prepare Data
Import images & labels
Convert formats · Review samples
02
Configure
Dataset + Model + Parameters
Reusable templates · Visual setup
03
Training Monitor
Run jobs · Track training
Progress · Loss · Metrics
04
Validate
Evaluate · Preview predictions
Inspect results · Assess readiness
05
Deliver Models
Export · Register versions
Select the active product model
Use validation results to refine data and configuration
Four vision tasks. One shared training platform.
Object Detection
Locate objects and defects
Image Classification
Recognize categories and quality
Semantic Segmentation
Map regions and boundaries
Anomaly Detection
Learn from normal samples
Simplify adoption / Reuse training knowledge / Build model assets
Notes: The workflow combines repository examples and conceptual detection graphics. Napari is the companion desktop segmentation annotation tool, separate from the web rectangle annotation tool. Export support varies by backend; PaddleClas has no platform export entrypoint. Model release registers configurations and weights, versions and the active model; it does not automatically deploy to production machines. The feedback path represents a user revising data and configuration.
These are training-platform capabilities. Integration into SwiftFlow requires runtime adaptation and acceptance.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 14
CHAPTER 03 / HAWKEYEPLUS
Object Detection | Industrial Defect Localization
Locate defects and identify their classes with bounding boxes and confidence scores
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
14 / 20
Locate & Classify Defects
Output: Boxes · Classes · Confidence
Illustrative output, not a model prediction
PaddleDetection
7 presets
PP-YOLOE · YOLOv3 · PicoDet · RT-DETR
Faster R-CNN · RetinaNet · CenterNet
TorchDet
4 presets
Faster R-CNN · RetinaNet · FCOS · SSD / SSDLite
SSD variants: VGG16 → SSD300; MobileNetV3 → SSDLite320
COCO Images & Labels
Box labels · Classes
Training & Metric Tracking
mAP / mAP50 · Training curves
Detection Preview
Locate defects · Inspect classes
Presets are backend-specific; PP-YOLOE and RT-DETR are not TorchDet models.
Notes: Detection models are read directly from DETECTION_PRESETS and TORCH_DET_PRESETS. PaddleDetection has seven preset families; TorchDet has four. SSD/VGG16 uses SSD300; SSD/MobileNetV3-Large uses SSDLite320. TorchDet supports COCO detector-head transfer for Faster R-CNN, RetinaNet and FCOS; SSD falls back to ImageNet backbone initialization. PP-YOLOE, YOLOv3, PicoDet, RT-DETR and CenterNet are not TorchDet families. Defect boxes are illustrative, not inference results or benchmark evidence.
These are training-platform capabilities. Integration into SwiftFlow requires runtime adaptation and acceptance.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 15
CHAPTER 03 / HAWKEYEPLUS
Segmentation Models | Pixel-level Understanding
TEM images illustrate segmentation across compact, encoder-decoder and Transformer architectures
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
15 / 20
Pixel-level Prediction Example
Regions · Boundaries · Label masks
TEM segmentation example from this project
PaddleSeg
7 presets
PP-LiteSeg · BiSeNetV2 · OCRNet · UNet · DeepLabV3+
SegFormer-B0 · FCN
TorchSeg
4 presets
UNet · DeepLabV3 (UI: DeepLabV3+) · FCN · LR-ASPP
TorchSeg maps DeepLabV3P to torchvision DeepLabV3, not a V3+ decoder.
Dataset Layout
Images + masks + train / validation splits
Evaluation Metrics
mIoU · Dice · Accuracy
Applications
Defect regions · Microstructure · Boundaries
Notes: PaddleSeg has seven current UI architectures. TorchSeg has four UI presets. The TorchSeg UI calls one preset DeepLabV3+ (config key DeepLabV3P), but the runtime uses torchvision DeepLabV3 without a V3+ decoder. DeepLabV3 is also a runtime alias, not a fifth UI preset. TEM images are project examples, not a benchmark for all models.
These are training-platform capabilities. Integration into SwiftFlow requires runtime adaptation and acceptance.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 16
CHAPTER 03 / HAWKEYEPLUS
Classification & Anomaly Detection
From image-level labels to learning normal appearance, reuse the same model-development workflow
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
16 / 20
PaddleClas | Image Classification
Learn labeled categories; predict image-level classes
Illustrative classification
9 Classification Variants
ResNet18 · ResNet34 · ResNet50 · ResNet101
MobileNetV3 Small / Large (x1.0)
PP-LCNet x1.0 · PP-HGNet Small
Swin Transformer Tiny (patch4 / window7 / 224)
TorchAnomaly | Anomaly Detection
Learn normal appearance; produce anomaly scores and heatmaps
Illustrative anomaly heatmap
5 anomalib Presets
PatchCore · PaDiM · STFPM · EfficientAD
SuperSimpleNet
Current UI presets only; custom YAML compatibility depends on the selected backend.
Notes: The nine PaddleClas choices are listed by exact configuration name in Supported_Models.md. The five TorchAnomaly presets are PatchCore, PaDiM, STFPM, EfficientAD and SuperSimpleNet. Training uses normal images. ReverseDistillation is not a current UI preset. Classification and anomaly images are conceptual illustrations. Environment/version compatibility still applies.
These are training-platform capabilities. Integration into SwiftFlow requires runtime adaptation and acceptance.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 17
CHAPTER 04 / OVERVIEW
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
17 / 20
04
Integrated Delivery
From development results to production readiness
How do delivery packages and joint validation connect both platforms?
04.1
Adaptation & acceptance
04.2
Shared delivery assets
04.3
Results & version traceability
SwiftFlow + HawkeyePlus | One shared method, two complementary platforms
Notes: Chapter transition: Integrated Delivery. Focus: From development results to production readiness. Guiding question: How do delivery packages and joint validation connect both platforms?.

## Slide 18
CHAPTER 04 / INTEGRATED DELIVERY
Connect Development and Production with a Standard Handoff
Adapt and jointly validate model deliverables before using them in inspection or measurement workflows
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
18 / 20
HawkeyePlus
Validated model & version
SwiftFlow
Inference & decisions in the workflow
Adaptation & joint acceptance
Match the input
Image shape, channels and preprocessing
Match the output
Labels, thresholds and output decoding
Validate on site
Independent samples, measurement references and timing
Recommended delivery baseline
Hardware baseline
Setup · Calibration · References
Workflow
Steps · Parameters · Rules
Model package
Version · Labels · Thresholds
Acceptance
Samples · Evidence · Records
Notes: Use a model handoff package and joint acceptance. HawkeyePlus exports supported inference artifacts and registers product versions with an active-model query API. SwiftFlow currently implements ONNX (including the YOLO path) and Paddle backends. Its configuration includes labels, input shape, channel order, normalization, thresholds and output decoding. Training support is not direct runtime compatibility: verify operators, I/O and preprocessing/postprocessing per model. Torch checkpoints are not direct inference artifacts; TorchSharp is reserved, and the current task enum has detection, classification and segmentation, but no dedicated anomaly decoder. Anomaly deployment needs additional adaptation. No existing automatic registry synchronization or feedback connector is assumed. The delivery baseline is a proposed engineering convention.
Sources and interpretation:
HawkeyePlus: docs/ARCHITECTURE.md; docs/FEATURES.md; src/lib/model-yaml.ts; model registry routes.
SwiftFlow: docs/Architecture.md; docs/Flow_Engine_Internals.md; InferenceSessionFactory.cs; ModelInstanceConfig.cs.
Illustrations and project examples are not performance, accuracy or production-acceptance evidence. Native text, panels and lines are editable; pictures are independently replaceable.

## Slide 19
SUMMARY / KEY TAKEAWAYS
Build a Reusable Standard Workflow
Organize engineering around a shared method, complementary platforms and a defined delivery baseline
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
19 / 20
One engineering method
Start with inspection or measurement goals
Define inputs and outputs across disciplines
Two complementary platforms
SwiftFlow connects equipment and execution
HawkeyePlus develops and validates models
A standard delivery baseline
Deliver configuration, models and evidence
Validate on site and retain versions and results
Define the goal → Engineer the solution → Validate jointly → Deliver traceably
The goal: help users deliver inspection and measurement through a consistent engineering approach
Notes: Recap three ideas: one engineering method, two complementary platforms and a standard delivery baseline. Emphasize clear inputs, outputs and acceptance evidence, with reusable configuration and model assets. The recommended engineering method is distinct from an automatic software connector.

## Slide 20
SWIFTFLOW + HAWKEYEPLUS
SwiftFlow + HawkeyePlus | Industrial Vision Engineering
WD CONFIDENTIAL
20 / 20
Thank You
Questions & Discussion
From hardware design to inspection and measurement delivery
Which use case should we prioritize?
How should we define acceptance and delivery?
Which workflows, models and knowledge can we reuse?
One shared method · Two complementary platforms · Reusable engineering deliverables
Notes: Close the presentation and discuss priority use cases, acceptance and delivery baselines, and reusable workflows and models. The discussion prompts do not imply an agreed implementation scope or production commitment.